## Slide 1: Introduction to MATLAB for Engineers
Louise Brown
http://moodle.nottingham.ac.uk/course/view.php?id=12439

## Slide 2: The MATLAB Desktop
Workspace
window
Command
History
window
Current folder
window
Command
window
To change path use dialog given by Environment->SetPath
path(‘Folder’,path) or path(path,’Folder’)
Function browser
Notes: Run up matlab
Command window – interactive scratchpad
Maths & other expressions fx
Current folder – drop down menu above allow it to be changed – probably want to set to Z drive – show setting to Z drive
Load & save by default to/from this folder
Type path
path( ‘Folder’, path) or path(path,’Folder’) to add to path – eg if created library of functions in a given folder
Workspace window – shows all variables currently in memory for the matlab session
Command history – commands executed in both current and previous sessions
Start button – quick access to tools and toolboxes
File->Preferences.. - change font size

## Slide 3: Changing the desktop configuration
Dock and undock windows
Slide window to tabbed position at side of window
Restore maximised window to tiled position
Stack windows by dragging the title bars over each other
Save setup: Desktop -> Save Layout.
Restore default layout: Desktop->Desktop Layout->Default
At top right hand corner of window gives drop down menu with options:
Notes: Try
Might want different configurations for different computers, no of screens etc

## Slide 4: Variables
All variables in MATLAB are stored as arrays
Scalar is 1x1 array
Vector is 1xn or nx1 array
Matrix is mxn array
…and so on for multi-dimensional arrays
Variables are created using an assignment statement
>> a = 10 creates a scalar variable
All variables are displayed in the workspace window
who – gives list of variable names
whos - gives name, size, type and memory size
Notes: MATrix LABoratory
NB Don’t need to declare variable
Move to Matlab and show creating variable
Double click in workspace window to open variable editor
Show who and whos
Be aware all variables stay in workspace until cleared – clear
Clear var
Clc to clear command window
Variables default to double

## Slide 5: String variables
Create character strings using single quotes
string = ‘Here is a string’
Stored as 1x16 char array
Type help strings for more information, or doc strings for full documentation
Notes: Demonstrate string
String stored as 2 bytes
Always use ‘help’ for quick documentation and ‘doc’ for full documentation

## Slide 6: Variable display format
Use format command to change display format
format long - fixed point format with 15 digits
format short – fixed point format with 4 digits
Note that format does not affect the way in which the variable is stored in memory
Type help datatypes to see other available data types
Notes: Defaults to short
Type pi, then change to format long
Try typing help format
Can use classes given in datatypes to specify type or can use cast function

## Slide 7: Variable Names
Must start with a letter but may include _ and numbers
Case sensitive
Certain reserved words cannot be used. Type iskeyword to see these
Built in function names may be used but this will block access to the original functions. (Clear workspace to restore)
Beware of overwriting pi, i and j
  i and j are used as complex numbers by default
  Type i or j at the command prompt
  0 + 1.0000i
Notes: Relate overwriting built in function names to path
A = sin(pi)
Sin = 2
A = sin(pi) - gives error because sin now defined as 1x1 array and pi isn’t valid index into it
Clear sin - clears sin from workspace so original definition now accessible
A = sin(pi) now works
If unsure of name use exist name to check not already in use
Use indices other than i or j if using complex numbers
Try creating string & variable

## Slide 8: Saving Workspace Data
MATLAB format:
Variables in the workspace can be saved to a file using the Save Workspace button or by typing save <filename> at the command line
Using save(‘filename’, ‘var1’, ‘var2’,…) allows selected variables to be saved
Saves with .mat extension in format readable by MATLAB
Has advantage that it is operating system independent
ascii format:
Use a ‘-ascii’ parameter to save data in ascii format.
>> save('Data.dat','x','y', '-ascii')
Conventionally a .dat file extension is used
Notes: Show save TestSave to .mat format
Clear workspace then double click or load
Advantage that operating system independent

## Slide 9: Vectors
>> A = [1 2 3 4]
>> A = [1,2,3,4]
Both give 1x4 vector
A =
1 2 3 4
>> A = [1:4] Colon operator gives regularly spaced elements
Increment can be decimal as well as integer
>> C = [1:0.2:2] gives
C =
1.0000 1.2000 1.4000 1.6000 1.8000 2.0000
Specify increment using format [first:step:last]
>> B = [1:2:9] gives B = 1 3 5 7 9
Notes: Create vectors using square brackets
Note colon operator step does not have to be integer
Show creating vectors and show in workspace

## Slide 10: More Vectors
Create a vector with a given number of equispaced points using
linspace( start, end, number of elements)
>> vec = linspace( 1, 8, 5 )
vec = 1.0000 2.7500 4.5000 6.2500 8.0000
logspace can be used to create logarithmically spaced points
y = logspace(a,b,n) generates n points between decades 10a and 10b
>> vec = logspace(1,2,5)
vec =
10.0000 17.7828 31.6228 56.2341 100.0000
Notes: Explanation that this is a function – difference between function parameters and separators in array
Also logspace

## Slide 11: Column Vectors
Either semicolon operator
>> A = [1;2;3;4]
or transpose operator
>> A = [1:4]’
A =
1
2
3
4
can be used to create a column vector:
Notes: Semicolon operator moves to a new row

## Slide 12: Indexing Vectors
A = 1 3 5 7 9 11 13
Subscript notation: A(3) gives 5
Subscript can be a vector: A([1 4 6]) gives 1 7 11
Colon notation to extract range: A(2:5) gives 3 5 7 9
Use ‘end’ either on its own or in range: A(4:end) gives 7 9 11 13
Replace element using index on left: A([1 3 5]) = [10 20 30]
A = 10 3 20 7 30 11 13
Notes: Various ways of indexing into array..
Note index starts from 1
Vector subscript – result is a vector
Explanation/demonstration of assignment – show that the number of elements being replaced on the left must be the same as those supplied on the right
Lot of rules apply to matrices as well so if can grasp on vectors will make those easier
Exercise 2.1 p.10

## Slide 13: Exercise 2.1
1) >> A = [5:2:17]
A =
5 7 9 11 13 15 17
2) >> B = [3:-1:-3]'
B =
3
2
1
0
-1
-2
-3
3) >> C = A([1 4 6])
C =
5 11 15
4) >> B([3 5 7]) = C
B =
3
2
5
0
11
-2
15

## Slide 14: Arithmetic Operations
Addition a + b
Subtraction a – b
Multiplication a * b for matrix or scalar multiplication
a.*b for element by element multiplication
Division a / b for matrix or scalar division
a./b for element by element division
Left division a \ b for matrix or scalar left division
a.\b for element by element left division
Exponentiation a ^ b for matrix or scalar exponentiation
a.^b for element by element exponentiation
Notes: Click 1: matrix and scalar multiplication
Click 2: element by element
Click 3: left division
Explain in more detail in next slides

## Slide 15
Order of Precedence
Arithmetic operations will be carried out in the order:
Evaluate parentheses working from inside to outside
Exponential operations (^)
Multiplication (*) and division (/) from left to right
Addition (+) and subtraction (-) from left to right
Notes: Example 2^2+3*4+5

## Slide 16: Addition and Subtraction Operations
Scalar addition and subtraction performs the operation on each member of the vector or array:
>> A = [1:4]
A =
1 2 3 4
>> A = A + 10
A =
11 12 13 14
Array addition and subtraction is performed element by element
>> B = [5:8]
B =
5 6 7 8
Note – this is achieved without using a loop
>> A = A + B
A =
16 18 20 22
Notes: Start to emphasise advantage of not having to use loops
Matlab interpreted language
Array operations optimised

## Slide 17: Multiplication Based Operations
Multiplication ( and /,\,^) operate element by element on scalars in the same way as the addition operator.
>> A = [1:4]
A =
1 2 3 4
>> A = A * 10
A =
10 20 30 40
Notes: Scalars – multiply, divide each element by number same as +-

## Slide 18: Multiplication Based Operations
To multiply vectors or arrays element by element the ‘dot’ operators must be used. Note that vectors must be the same size.
>>A = [1:4]
A =
1 2 3 4
>> B = [2:5]
B =
2 3 4 5
>> D = A.*B
D =
2 6 12 20
Note that just using the * operator here will result in an error
Notes: Scalars – multiply, divide each element by number same as +-
Normal matrix multiplication won’t work on these vectors

## Slide 19: Multiplication Based Operators
Using multiplication based operators without a dot operator will result in standard matrix operations
>> A = [1:4]
A =
1 2 3 4
>> B = [1:4]'
B =
1
2
3
4
So that
>> A*B
ans =
30
but
>> B*A
ans =
1 2 3 4
2 4 6 8
3 6 9 12
4 8 12 16
1 x 4 * 4 x 1
Inner dimensions must match
Outer dimensions give final size
Notes: Note that matrix multiplication is order dependent
Error – Inner matrix dimensions must agree

## Slide 20: Vectors as Function Input
Vectors can be used as input arguments to functions – both built-in and user defined
>> A = [0:pi/6:pi]
A =
0 0.5236 1.0472 1.5708 2.0944 2.6180 3.1416
>> B = sin(A)
B =
0 0.5000 0.8660 1.0000 .8660 0.5000 0.0000
Notes: Exercise 2.2 p.13

## Slide 21: Exercise 2.2
1) >> 1/(2+3^4) + 5/(6*7) + 7/8
ans =
1.0061
2) >> A = linspace( 0, 2*pi, 9 )
A =
0 0.7854 1.5708 2.3562 3.1416 3.9270 … 4.7124 5.4978 6.2832
>> SinAng = sin(A)
SinAng =
0 0.7071 1.0000 0.7071 0.0000 -0.7071 … -1.0000 -0.7071 -0.0000
3) >> SinAng = SinAng + 1
SinAng =
1.0000 1.7071 2.0000 1.7071 1.0000 0.2929 0 0.2929 1.0000

## Slide 22: Exercise 2.2
4) >> B = [1:9]
B =
1 2 3 4 5 6 7 8 9
>> SinAng.*B
ans =
1.0000 3.4142 6.0000 6.8284 5.0000 1.7574 0 2.3431 9.0000

## Slide 23: Left Division
a\b = a-1b for matrix operations
a.\b = b/a when performed element by element on arrays or when one of the operands is a scalar
>> A = [1:4]
A =
1 2 3 4
>> A.\2
ans =
2.0000 1.0000 0.6667 0.5000
Notes: Left division has two definitions:
When would you use a.\b?

## Slide 24: Using Left Division to Solve Simultaneous Equations
The pair of simultaneous equations
3x1 + 2x2 = 12
x1 + 4x2 = 14
can be written as Ax = B
where , , and
Solving using linear algebra gives x = A-1B
In MATLAB set up the arrays
>> A = [3 2; 1 4]
A =
3 2
1 4
>> B = [12;14]
B =
12
14
and solve using the left division operator
>> x = A\B
x =
2
3
Notes: Next slide will cover setting up matrices
Going to do an example but will just cover creating matrix first

## Slide 25: Matrices
Use the semicolon operator to separate the rows of a matrix
>> A = [1 2 3 4 5; 5 6 7 8 9]
A =
1 2 3 4 5
5 6 7 8 9
The colon operator can be used as for vectors.
The same result is given by
>> A = [1:5;5:9]
Notes: Think of matrix as a stack of row vectors
Must have same number of elements in each row
Now have a go at solving simultaneous equations with Exercise 2.3 p.14

## Slide 26: Exercise 2.3
>> A = [1 2 3; 2 3 -1; 4 -1 2]
A =
1 2 3
2 3 -1
4 -1 2
>> B = [13;4;13]
B =
13
4
13
>> X = A\B
X =
2.0000
1.0000
3.0000

## Slide 27: Character Matrices
Arrays of characters must have the same number of elements in each row.
>> charArray = [‘ONE';‘SEVEN';‘FIVE']
Error using vertcat
Dimensions of matrices being concatenated are not consistent.
O | N | E |  | 
S | E | V | E | N
F | I | V | E | 
Notes: Note can create arrays of strings if all same length
Will come back to more straightforward way of storing different length strings later

## Slide 28: Character Matrices
Use char function to create arrays with padded strings
>> charArray = char('one','seven','five')
charArray =
one
seven
five
Creates 3x5 char array with spaces padding shorter strings
O | N | E |  | 
S | E | V | E | N
F | I | V | E | 

## Slide 29: Matrix Indexing
A = 1 2 3 4 5
5 6 7 8 9
9 10 11 12 13
Subscript notation: A(3,2) = 10
Colon notation to extract range in both rows and columns: A(2:3, 3:4) = 7 8
11 12
Colon notation to extract whole row or column: A(2, : ) = 5 6 7 8 9
Or several rows or columns: A( : , [1 3 5]) = 1 3 5
5 7 9
9 11 13
row
column
Notes: Use subscript notation as for vectors with row, column specification
Think of : on its own as ‘all rows’ or ‘all columns
Ask how would extract some examples?
How would you extract scattered elements? -> linear indexing

## Slide 30: Linear Indexing
A = 1 1 2 4 3 7 4 10 5 13
5 2 6 5 7 8 8 11 9 14
9 3 10 6 11 9 12 12 13 15
Linear index is obtained by counting down each column in turn
Linear index: A(5) = 6
Find indices for elements (1, 3) and (2, 4)
Use sub2ind( size, row vector, column vector )to convert from subscript to linear index
>> Index = sub2ind( size(A), [1 2], [3 4] )
Index =
7 11
Then extract actual elements using the linear index vector: A(Index) = 3 8
Notes: Needed if want to extract scattered elements of matrix
Size(A) returns the number of rows and columns
index = sub2ind(sizeA, [1 2], [3,4])
Show A(index) = A(index)+0.1

## Slide 31: Combining Matrices
Larger arrays can be built up from smaller ones:
>> A = [1:5;5:9]
A =
1 2 3 4 5
5 6 7 8 9
>> B = [1:2:9;2:2:10]
B =
1 3 5 7 9
2 4 6 8 10
>> D = [A;B]
D =
1 2 3 4 5
5 6 7 8 9
1 3 5 7 9
2 4 6 8 10
>> E = [A B]
E =
1 2 3 4 5 1 3 5 7 9
5 6 7 8 9 2 4 6 8 10
Note that the dimensions of arrays being joined must be consistent.
Notes: Effectively same as the way that vectors are stacked to make matrices
Could also have put side by side: [A B]

## Slide 32: Matrix Functions
A = 1 2 3 4 5
5 6 7 8 9
length(X) returns the largest dimension of an array: length(A) = 5
size(X) returns a vector containing the length of each dimension of the array: >> dims = size(A)
dims =
2 5
The rows and columns can also be returned as separate variables:
>> [row,column] = size(A)
row =
2
column =
5
Notes: Take a look at some useful matrix functions:
If use [row,column] = size(A) can get separate variables for row & column – demonstrate?
Same result for vector if returning single argument

## Slide 33: Useful automatically generated matrices
Identity matrix: eye(X)
>> eye(2)
ans =
1 0
0 1
All ones: ones(m, n, p…)
>> ones(2,3)
ans =
1 1 1
1 1 1
All zeros: zeros(m, n, p…)
>> zeros(3,2)
ans =
0 0
0 0
0 0
Only one parameter as the identity matrix is square
p… for matrices of more than two dimensions
Notes: Note identity matrix only one parameter as must be square
Note the p dimension as can have more than 2D matrices

## Slide 34: Matrix Memory Management
Extra elements may be added to an array simply by allocating an element at a given position
A = 1 2
3 4
Adding an element at (5,5) grows the array:
>> A(5,5) = 10
A =
1 2 0 0 0
3 4 0 0 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 10
A new block of memory will be allocated each time extra elements are added to the array – this is slow!
If the final size of the array is known create an array of the final size (typically using the zeros() function) and then assign elements as required
Notes: Need to be careful how matrices are specified
If have array A…and add element (5,5) will grow array and reallocate memory
If have loop which adds one element each time will do the same
Copy is made of data in order to move. If have v large data set may have problems -> 2 copies in memory during copy operation
Can then use sparse array in functions as normal

## Slide 35: Sparse Arrays
For arrays with large numbers of zero elements the sparse(N) function can be used to squeeze out zero values.
A =
1 2 0 0 0
3 4 0 0 0
0 0 0 0 0
0 0 0 0 0
0 0 0 0 10
sparse(A) reduces the size of A from 200 to 84 bytes
Notes: Demonstrate
Exercise 2.4 p.19

## Slide 36: Exercise 2.4
1) >> A = [9 12 13 0;10 3 1 5;2 5 10 3]
A =
9 12 13 0
10 3 1 5
2 5 10 3
>> B = [1 4 2 11;9 8 16 7;12 5 0 3]
B =
1 4 2 11
9 8 16 7
12 5 0 3
2) >> C = A(3,3)
C =
10
>> D = A(:,3)
D =
13
1
10
>> E = [B(1,:);B(3,:)]
E =
1 4 2 11
12 5 0 3
>> F = [A;B]
F =
9 12 13 0
10 3 1 5
2 5 10 3
1 4 2 11
9 8 16 7
12 5 0 3
>> G = [A(:,1) B(:,4)]
G =
9 11
10 7
2 3

## Slide 37: Exercise 2.4
3) >> E(2,2) = 20
E =
1 4 2 11
12 20 0 3
>> A(1,:) = 0
A =
0 0 0 0
10 3 1 5
2 5 10 3
>> F(:,3) = 1:6
F =
9 12 1 0
10 3 2 5
2 5 3 3
1 4 4 11
9 8 5 7
12 5 6 3
>> A(:,1) = B(:,2)
A =
4 0 0 0
8 3 1 5
5 5 10 3

## Slide 38: Scripts
Script files are created by selecting New Script or typing ‘edit’ at the command prompt.
MATLAB script files are saved with a ‘.m’ extension (by default to the current folder)
Scripts are run by typing the script name at the command prompt
Comment lines start with %
The first comment line in a script is the H1 line which is used as a help for the script.
A semicolon at the end of the line will suppress output to the monitor
Notes: Emphasise everything done so far been in workspace - transient
Show creating script ( ScriptExample.m)
% Test script to calculate square roots
% Second H1 line
% Script body
A = [1:10];
A = sqrt(A); %Type squr[A] – gives error for bracket but not squr until run
Show help
Show running from command prompt
NB no output as used semicolons
*Recap what actually done:
Created script in file ScriptExample.m
Run, correcting errors
Show, saved in current folder
Emphasise if asked to create script that need to create in editor and save

## Slide 39: Simple User Input
Use input(str) command to fetch user input
>> value = input( ‘Enter a value: ‘);
Enter a value:
A second parameter ‘s’ indicates the input is a character or string.
>> str = input('Input yes or no ','s')
Input yes or no yes
str =
yes
User input
10
Notes: Change square root script to input max value
maxVal = input('Input max value ');

## Slide 40: Output
Use the disp(str) function for simple output
To display a variable use disp(A)
Or to output a string:
% Create a string
str = 'Output from disp function‘;
% Pass the string as a parameter to the disp function
disp( str );
>> Output from disp function
Notes: Add disp(A) to script example
Str = [‘The ‘ num2str(maxVal) ‘values of A are: ‘ num2str(A)];

## Slide 41: Output
Simple strings can be assembled to give output data.
Use the num2str function to convert numerical data into a string
>> Vel = 20;
>> strTitle = ['Starting speed = ' num2str(Vel) ' m/s'];
>> disp(strTitle);
Starting speed = 20 m/s
Notes: Add disp(A) to script example

## Slide 42: Freefall Script
Write a script called FreeFallExample.m which calculates the distance travelled by a freely falling object at ten time increments from release to time, t, using the equation
d = 0.5gt2
The time will be user input.
Output the distances calculated.
Notes: Preparation for exercise 4.1
t = 0 to t=input time at time increment t/10

## Slide 43: Freefall Script
Notes: Introduce idea of code planning/design
Get them to write down the steps involved in the example
Get into pairs to plan pseudocode?
Flowcharts
Pseudocode

## Slide 44: Exercise 4.1
Write a script called FreeFall.m which calculates the distance travelled by a freely falling object at each time increment between two given times using the equation
d = 0.5gt2
The start and end times and time increment will be user input.
Output the distances calculated.
(For more of a challenge present the output as two columns showing times and distances)
Notes: Exercise 4.1 p21

## Slide 45: Exercise 4.1

## Slide 46: Exercise 4.1
Input start time, end time, time increment and g
Create vector of times
Calculate distance for each time
Output times and distances

## Slide 47: Simple x-y plots
plot(x,y) plots vector x against vector y
>> t = 0:0.5:5
>> distance = [0, 0.2, 0.5, 0.73, 0.74, 1.2,… 1.5, 1.6, 1.7, 2.0, 2.33]
>> plot(t, distance, ‘o’)
Third parameter used to specify line style, marker type and colour
plot command automatically fits axes to the data.
To control axis scaling use: axis( [xmin, xmax, ymin, ymax])
Notes: Matlab really good for plotting data
x = linspace(-pi,pi,20)
points = sin(x)
plot(x,points,'o') and from workspace
Show if only use plot( sin(x) ) just plots against integer range
Point out different sorts of plot available

## Slide 48: Plot from Workspace
Select variables to plot
Select plot type from ribbon
Notes: Exercise 5.1 p23

## Slide 49: Annotating Figures
From the script:
>> xlabel( ‘Time, s’)
>> ylabel(‘Distance, m’)
>> title(‘Distance/Time graph’)
Note – plot command must be executed first
Or using Plot Tools:
Use Show Plot Tools and Dock Figure icon
Or type ‘plottools’ at the command prompt
Script for similar plots can be created using File->Generate code
Notes: Xlable(‘Time, s’)
Ylable(‘Distance, m’)
Title(‘Distance/Time graph)
Show plot tools on figure previously created – basically make aware that it’s there and they can investigate later
Show file->generate code

## Slide 50: Plotting Multiple Data Sets
Various methods of plotting multiple data sets on one figure:
hold on - any plot commands will plot on same figure until hold off is executed
Send multiple sets of data in one plot command
>> plot( t, distance, ‘s’, t, distance2, ‘o’ )
Collect multiple sets of data into one matrix
>> distances = [distance;distance2]
>> plot( t, distances, ‘o’ )
Creating multiple figures:
Select the current figure to be plotted to using the figure(n) command. Any subsequent plots will be performed on this figure

## Slide 51: Subplots
Several plots in the same window
Use subplot(m,n,p) command.
Window is split into grid of m rows by n columns .
p selects the window for plotting.
>> subplot(2,2,4)
% Call plot commands before calling subplot again for next location
p = 1 | p = 2
p = 3 | p = 4
Notes: Note that subwindows are numbered row by row rather than down columns like arrays

## Slide 52: Saving Figures
Save figures using saveas function:
saveas(gcf, ‘filename’, ‘format’)
returns the handle to the current figure
>> saveas( gcf, ‘Figure’,‘png’)
Saves to Figure.png
File->Save Saves a Matlab .fig file
File->Save As… Saves to standard image formats

## Slide 53: Exercise 5.2
Suggested initial values:
Start velocity = 60 m/s
Launch angle = pi/3
Plot horizontal distance on x-axis and vertical distance on y-axis
Format the title (to include the velocity and angle) using a vector of strings
Remember to convert the angle back into degrees to display in the title
Use num2str to create strings from variables to include in the string,
eg ‘30 degrees’
Notes: Exercise 5.2 p26
Don’t need user input – just specify values
Few things in here that you don’t know – make use of help/doc/web search
Plan before you start
*Show use of num2str + using help/function browser to find functions

## Slide 54: Debugging
3 types of errors: syntax, runtime and logical
Syntax errors:
At the command line an error message is displayed
In the edit window: orange bar – warning
red bar - error
Runtime errors:
Occur as code executes, eg out of bounds index
Within a script an error message is given including the line number
Note that in MATLAB divide by 0 does not generate an error – a value of Inf is assigned and the program continues to run
Logical errors:
Hardest to find. Program runs but gives incorrect results
In MATLAB can use Code Cells or the built-in debugger
Notes: disp('syntax error)
for k = 1:4
a(k) = a(k)+1
end

## Slide 55: Using the Built-in Debugger
Save and run (F5)
Set/clear breakpoint (F12)
Breakpoint
Right click on breakpoint to display options
Exit debug mode (Shift + F5)
Step (F10)
Step into (F11)
Step out (Shift + F11)
Continue (F5)
When running debug the menu is displayed:
Notes: Demonstrate debugger
Exercise 6.1 p.28

## Slide 56: Code Sections
Code Cell Demonstration
Insert section break
Run section options
To increment/decrement variable: Hover over value, right click and select Increment Value and Run Section from menu to give dialog
Notes: Not entirely focused on debugging but can see how being able to run individual cells will help to home in on errors
Exercise 6.2 – add code cells to projectiles script

## Slide 57: Program Structure
Sequential
Input
Calculation
Output
Selection
Input
Decision
Calc
Calc
true
false
Repetition
Decision
Input
Calc
true
false
Notes: So far only used sequential operations. Normally programs more complex.
Look first at Selection. Need some means of making decisions.

## Slide 58: Relational and Logical Operators
Logical data type: a = true or a = false – occupies 1 byte
convert to logical using b = logical(x)
Relational a < b less than
a <= b less than or equal to
a > b greater than
a >= b greater than or equal to
a == b equal to
a ~= b not equal to
Logical a & b and
a | b or
~ a not
xor( a,b ) exclusive or
Notes: B = logical(x) – gives true for any value other than 0

## Slide 59: Comparing Matrices
Comparisons on matrices will compare corresponding elements and create a matrix of the results using the logical data type
>> a = 1:5
a =
1 2 3 4 5
>> b = [3 1 2 4 0]
b =
3 1 2 4 0
>> a > b
ans =
0 1 1 0 1

## Slide 60: Logical Indexing
Relational and logical operators are performed element-wise on vectors or matrices resulting in a logical matrix:
    A = 1 2 3 4 5
    3 4 5 6 7
    >> B = A > 2 & A < 6
    B = 0 0 1 1 1
    1 1 1 0 0
Logical matrix B can be used as a mask to perform operations on selected elements of a matrix
>> A(B) = sqrt(A(B))
A = 1.0000 2.0000 1.7321 2.0000 2.2361
1.7321 2.0000 2.2361 6.0000 7.0000
Notes: Again no need to use loop to perform operation on elements which satisfy condition
Break into steps: Create B, A(B), A(B) = 10*ans

## Slide 61: Logical Indexing(2)
    A = 1 2 3 4 5
    3 4 5 6 7
Extract the elements which satisfy the test: >> C = A(B)
                C =
                3
                4
                3
                5
                4
                5
    B = 0 0 1 1 1
    1 1 1 0 0
To find the indices of the elements which satisfy the test use the find() function
>> D = find(A>2 & A<6)
D =
2
4
5
6
7
9
Notes: Test a>2 & a<6
Extract the elements which satisfy the condition
Find() function returns the indices

## Slide 62: find()
Index = find(x,1) – returns the linear index of the first nonzero element, or first element which satisfies a specified condition
>> B = [0 0 0 3 4 5 6]
B =
0 0 0 3 4 5 6
>> find( B,1 )
ans =
4
>> find( B>4, 1)
ans =
6
Notes: Find: Example of temperatures and want to find first that’s above certain value

## Slide 63: Floating Point Comparisons
Comparison of floats or doubles
Small differences resulting from floating point arithmetic may cause errors when checking for equality.
>> a = 0.5-0.4-0.1
a =
-2.775557561562891e-17
Use a tolerance check:
>> abs(a) < tolerance
A
0.9999999999
if ( A == 1) % will be false
Tol = 1e-6;
abs( A – 1.0 ) < Tol % will return true
Notes: Comparison of doubles – eg 1.0 may actually be 0.9999999 so ==1.0 no good
Exercise 8.1 p34

## Slide 64: Exercise 8.1
1) >> A = [9 12 18 0;10 3 1 7;2 5 14 22]
A =
9 12 18 0
10 3 1 7
2 5 14 22
>> B = A >=7 & A < 15
B =
1 1 0 0
1 0 0 1
0 0 1 0
2) >> A(B) = A(B).^2
A =
81 144 18 0
100 3 1 49
2 5 196 22
3) >> find(A>100)
ans =
4
9
4) >> B = A(A>100)
B =
144
196

## Slide 65: Conditional Statements
if condition
Code block
end
Age = 6;
if Age < 5
disp(‘a is less than 5’);
end
Note that if the condition is applied to an array it will only be true if all elements of the array satisfy the condition
Selection
if Age < 5
Display message
true
false
Age = 6
Notes: If statements work best with scalars. On array condition only true if true for every value. For array better to use find
NB. No brackets but need end. Indentation not necessary but better style

## Slide 66: Nested if statements
if statements can be nested:
if condition1
Code block 1
if condition 2
Code block 2
end % End of condition 2
Code block 3
end % End of condition 1
Remember the ‘end’ statement at the end of each code block
Indentation is not necessary but is good style and makes code more readable
if Age >5
Code Block 1
true
false
if Age < 10
Code Block 2
Code Block 3
true
false
Input Age
Condition 1
Condition 2
Notes: % Nested if
Age = input('Input age: ');
if Age > 5
disp( 'Age is greater than 5'); % Code block 1
if ( Age < 10 )
disp( 'Age is between 5 and 10'); % Code block 2
end
disp( 'Code block 3');
end

## Slide 67: if/else Statements
if condition 1
Code block 1
else
Code block 2
end
Age > 5
Message 2
true
Message1
else
Input Age
if age < 5
disp('Age is less than 5');
else
disp('Age is 5 or over');
end
Notes: Exercise 8.2 p35

## Slide 68: if/elseif/else Statements
if condition 1
Code block 1
elseif condition 2
Code block 2
else
Code block 3
end
Age > 5
Message 1
elseif
true
Age < 11
Message 2
Message 3
else
true
Input Age
Notes: AgeElseIf.m

## Slide 69: if/elseif/else Statements
if age < 5
disp('Age is less than 5');
elseif age < 11
disp('Age is between 5 and 10');
else
disp('Age is 11 or over');
end
Don’t overspecify conditions:
elseif age < 11 & age >=5 - second condition is redundant
elseif age < 11 & age >5 - would give incorrect result for age = 5
Notes: Don’t overspecify conditions – don’t need 2nd condition age > 5 (would result in incorrect output for 5)
Exercise 8.3

## Slide 70: Switch Statement
switch variable
case value1
Code block 1
case value2
Code block 2
…
case value n
Code block n
otherwise
Code executed if expression none of
values specified
end
%Menu and switch/case statement example
Colour = menu('Select Colour', 'Red', 'Blue', 'Green');
switch Colour
case 1
disp('You chose red');
case 2
disp('You chose blue');
case 3
disp('You chose green');
otherwise
disp('You didn''t make a selection');
end
Notes: Variable can be scalar or string (or cell array – come to later)
Doesn’t fall through so no need for break
Demonstrate menu program – MenuSwitchExample.m – run in debugger

## Slide 71: Repetition Operators
Repetition
Decision
Input
Calc
true
false
For loop:
Use to iterate through a given set of values (given by an index matrix)
While loop:
Loop until a specified condition is satisfied
Notes: Get them to think about when they might use a loop in a program
Iterating through pre-defined range – for loop
Until condition is satisfied – while loop eg until tolerance satisfied in iterative method or until valid input is entered

## Slide 72
for t = 1:0.1:2
Calculate distance
Increment k
k = 1
for index = [matrix]
Code block
end
k = 1;
for t = 1:0.1:2
% Calculate distance in freefall
d(k) = 0.5 * 9.81 * t^2;
k = k+1;
end
Note that step doesn’t have to be integer
This will grow the array d by one element on each iteration
for Loops
Notes: Demonstrate with debugger – show vector growing. Show red squiggly line for code tip
Clear first!
ForLoopGrowingVector.m
k = 1;
for t = [1 1.25 1.5 1.75 2]
% Calculate distance in freefall
d(k) = 0.5 * 9.81 * t^2;
k = k+1;
end
Using vector for i = [1 3.4 7]

## Slide 73: for Loops
for index = [matrix]
Code block
end
k = 1;
for t = 1:0.1:2
% Calculate distance in freefall
d(k) = 0.5 * 9.81 * t^2;
k = k+1;
end
Note that vectorised form is much more efficient:
t = [1:0.1:2];
d = 0.5 * 9.81 * t.^2;
If 2D matrix the index will contain a column of the matrix for each iteration of the loop – ie a column vector
Notes: Note if have matrix as index then whole column is used as index each time through loop
Might use for loop if going through set of filename where manipulating string
ForLoop2D.m - note that vectorised version would still work if t is 2D matrix

## Slide 74: tic/toc
tic
Some code
.
.
.
toc
Elapsed time is 0.000039 seconds.
Times the code executed between the tic and toc commands
Notes: Exercise 9.1 p37

## Slide 75: while Loops
while condition==true
Code block
end
Use while loop to input values
and calculate an average
count = 1;
num = input('Input first number: ');
% negative number terminates loop
while num >= 0
numbers(count) = num;
count = count + 1;
num = input('Input next number: ');
end
average = mean(numbers);
disp(['Average is ', num2str(average)]);
num >= 0 ?
Increment count
input num
input num
add num to vector
true
false
Calculate average
Display average
count = 1
Notes: Average.m
Break – to exit loop
Continue – to proceed to next iteration of loop

## Slide 76: Exercise 9.2
Change the Projectiles script to loop until a valid input has been entered.
What sort of loop will be used?
While loop – continuing until condition is satisfied
Probably need to set angle to an invalid value to start so that the loop is executed at least once
Notes: How do you decide between for/while loops?
Exercise 9.2 p38

## Slide 77: Functions
function [argout1, argout2..] = funcName( argin1, argin2,..)
% H1 comment line
% Other comments
Code Block
(return)
(end)
Must be the same as the filename – funcName.m
Dummy input arguments
Must have function declaration
Dummy output arguments
Optional
Notes: Built up basics to be able to write code
Need the tools to be able to write well constructed programs
Good practice to include H1 line to show input/output arguments
Dummy arguments are basically templates

## Slide 78: Calling Functions
Called from a script or the command window by using the function name
distance = DistBetweenPoints( x1, y1, x2, y2 );
Use square brackets on the left for functions which return more than one value
[row, column] = find(4 )
The function .m file cannot be run on its own.
Note – parameters are passed by value. A copy of the arguments is passed to the function
Notes: DistBetweenPoints.m pass p1x etc so can see different to x1 etc in function workspace
distance = DistBetweenPoints( x1, y1, x2, y2 );

## Slide 79: Functions and Arrays
Arrays can be passed as parameters to and from functions
Ensure that any multiplication based operations within the function use the dot operator
Notes: Call DistBetweenPoints with arrays – then change to .^
Exercise 10.1 p39

## Slide 80: Subfunctions
Can have several functions in one file:
First function is primary function and has same name as filename
Subfunctions follow in the same file and are only visible to other functions in that file (equivalent to private functions in C++)
Help still provided by H1 line but accessed using >
>> help myFunction>mySubFunc

## Slide 81: Anonymous Functions
Anonymous functions are local functions only available until the workspace is cleared
Fnhandle = @ (input arguments) functioncode;
Shows function handle being created
logfunc = @(x) log(x) + x
Can be saved in .mat file using load and save commands
>> logfunc(2.3)
ans =
3.1329
Notes: Bit like an inline function
Show creating polynomial poly = @(x) 4*x.^2 + 3.*x + 7

## Slide 82: Function Functions
Function functions take another function as input:
fplot( @sin, [-pi,pi] ); plot sin in range –pi to pi
Obtains function handle
fplot( logfunc, [1,100] )
Already function handle, doesn’t need @
Notes: Logfunc is anonymous function from previous slide
[-pi pi] gives vector containing the xmin and xmax values

## Slide 83: Persistent variables
Local variables are cleared when exit from functions
Persistent variables remain between function calls
  persistent count
  % Check if count has been initialised and set to 0 if not
  if isempty( count )
  count = 0;
  end
  count = count + 1;
declare variable, initialized to empty matrix
Clear persistent variables from memory using clear functions
Persistent variable name must not be the same as any other in the workspace
Notes: Similar to static variables in C++
Might use to check whether performed operation which only needs to be done once
Eg. read data from a spreadsheet
Exercise 10.2 p.41

## Slide 84: Exercise 10.2
>> poly1 = @(x) 3*x.^2 + 4*x +5;
>> plot([-10:10],poly1(-10:10) )
>> fplot(poly1, [0,20])
>> poly1(1:10)
ans =
12 25 44 69 100 137 180 229 284 345

## Slide 85: Tables
Useful for heterogenous, column oriented or tabular data
Variables can have different data types
All columns must have the same number of rows
Not restricted to column vectors (eg could have matrix but number of rows condition still applies
Create table from workspace data using the table function:
TableName = table(var1, var2, var3,… );
or by using readtable to load a data set:
TableName = readtable(‘data.dat’);
Notes: load patients
whos to show data
PatientData = table( Gender, Age, Height, Weight );
AllPatientData = readtable(‘patients.dat’);

## Slide 86: Indexing into Tables
Column data can be addressed using dot notation and then the normal indexing for the data type:
PatientData.Gender % Accesses the whole column
PatientData.Gender(10) % Accesses data in column
Access particular rows and columns using subscript notation:
PatientData(1:3, :);
ans =
Gender Age Height Weight
________ ___ ______ ______
'Male' 38 71 176
'Male' 43 69 163
'Female' 38 64 131

## Slide 87: Add, Remove and SaveTable Data
Extra data can be added by using a new column name and assigning it a data item with the correct number of rows:
PatientData.ID = (1:100)’;
Delete column using []
PatientData.ID = []
Table data can be written to a file using the writetable function:
writetable( PatientData, ‘PatientData.txt’);
Notes: summary(PatientData)

## Slide 88: Table Metadata
Table metadata is contained in table.Properties:
PatientData.Properties
ans =
Description: ''
VariableDescriptions: {}
VariableUnits: {}
DimensionNames: {'Row' 'Variable'}
UserData: []
RowNames: {}
VariableNames: {'Gender' 'Age' 'Height' 'Weight'}
Edit the metadata using dot notation for the relevant property:
PatientData.Properties.VariableUnits{'Height'} = 'inches‘
PatientData.Properties.VariableUnits
ans =
'' '' 'inches' ''
Notes: PatientData.Properties

## Slide 89: Cell Arrays of String Data
Cell arrays can store different types of data, accessed by index
Useful for storing strings of different lengths
CellArray = {'Age', 'Weight', 'Height'}
CellArray =
'Age' 'Weight' 'Height'

## Slide 90: Index Table Using Row Names
If the RowNames property has been set this can then be used as an index into the table:
PatientData.Properties.RowNames = LastName;
Data can then be selected by row name. Note that the row names are assembled into a cell array for use as the row parameter if more than one row is to be accessed:
PatientData({'Wilson', 'White'}, : )
Selections can also be made using the variable names:
PatientData(‘Russell’, {‘Height’,’Weight’} )
ans =
Height Weight
______ ______
Russell 69 188
Notes: Set row names & show variable window

## Slide 91: Plotting Data from Tables
Use dot notation to plot data for a whole column:
plot(PatientData.Age, PatientData.Weight, ‘xr’)
Logical indexing can be used to select data to plot. To plot data for just the males in the data set:
ind = strcmp( PatientData.Gender, 'Male');
plot(PatientData.Age(ind), PatientData.Weight(ind), 'xr')
Invert the selection to plot the data for females:
plot(PatientData.Age(~ind), PatientData.Weight(~ind), 'ob')
Notes: Exercise 11.1 page 43

## Slide 92: Importing Data
Import Wizard
Use the Import Data button
or right click on filename and select Import Data…
Data can be imported as row or column vectors where headers are present
Otherwise imported as matrix
Use Import Selection-> Generate Script or Generate Function to create code to reproduce import of the selected data
Also launch using
>> uiimport(‘SimonVega.jpg’)
Notes: Show import of Section0.txt using wizard
Show save as matrix, renaming variable names, changing type to text
Show cell array for text
Import Section0Columns.txt – imports x and y
Show import of SimonVega.jpg – show 3D array with RGB uiimport(‘SimonVega.jpg’)
show changing colours & plot
>> SimonVega(100:200, 100:200, 1) = 255;

## Slide 93: Cleaning Data
Bad or missing data will be imported as NaN
This can be removed using logical indexing
badData = isnan(Age);
CleanAge = Age(~badData);
Gives logical vector with value of 1 where data is NaN
Use ~ (not) so that good data has value of 1 in logical vector
Notes: Use Age.mat to demonstrate

## Slide 94: Before you leave, please complete the online course evaluation
To access the evaluation form visit:
https://nottingham.onlinesurveys.ac.uk/graduate-school-course-evaluation-survey
or using
http://tiny.cc/gradschooleval
Input the course date as 04/02/2019
Input the course code as GSTML1

## Slide 95: Publishing Code
Publishing Demonstration

## Slide 96: Toolboxes
Signal Processing
  https://uk.mathworks.com/products/signal.html
Image Processing
  https://uk.mathworks.com/products/image.html
Optimisation
  https://uk.mathworks.com/products/optimization.html
Symbolic Maths
  https://uk.mathworks.com/products/symbolic.html
Data Acquisition
  https://uk.mathworks.com/products/daq.html
Control System
  https://uk.mathworks.com/help/control/index.html
Curve Fitting
  https://uk.mathworks.com/products/curvefitting.html
Statistics and Machine Learning
  https://uk.mathworks.com/products/statistics.html

## Slide 97: More to Explore
Version Control using GIT – keep track of changes to your code
  https://uk.mathworks.com/help/matlab/matlab_prog/set-up-git-source-control.html
GUIDE – for generating user interfaces
  https://uk.mathworks.com/help/matlab/guide-or-matlab-functions.html
Profiler – use to find bottlenecks in programs and speed up code
  https://uk.mathworks.com/help/matlab/matlab_prog/profiling-for-improving-performance.html
Testing Frameworks – use to set up automated tests for your code
  https://uk.mathworks.com/help/matlab/matlab-unit-test-framework.html